## Slide 1: Kinematics

## Slide 2: Kinematics
The branch of mechanics concerned with the motions of objects without regard to the forces that cause the motion
Why kinematics?
  Hierarchical articulated model
  Posing a character

## Slide 3: Degrees of Freedom (DOF)
The minimum number of coordinates required to specify completely the motion of an object
6 DOF: x, y, z, raw, pitch, yaw
pitch
roll
yaw

## Slide 4: Degrees of Freedom in Human Model
Root: 3 translational DOF + 3 rotational DOF
Rotational joints are commonly used
Each joint can have up to 3 DOF
  Shoulder: 3 DOF
  Wrist: 2 DOF
  Knee: 1 DOF
1 DOF
3 DOF

## Slide 5: Revolute Joints
3 DOF joint
  gimbal
  ball and socket
2 DOF joint
  universal

## Slide 6: Hierarchical Articulated Model
Represent an articulated figure as a series of links connected by joints
Enforce limb connectivity in a tree-like structure
root

## Slide 7: Joint Space vs. Cartesian Space
Joint space
  space formed by joint angles
  position all joints—fine level control
Cartesian space
  3D space
  specify environment interactions

## Slide 8: Forward and Inverse Kinematics
Forward kinematics
  mapping from joint space to cartesian space
Inverse kinematics
  mapping from cartesian space to joint space
Forward Kinematics
Inverse Kinematics

## Slide 9: Forward and Inverse Kinematics (cont.)
Forward kinematics
  rendering
Inverse kinematics
  good for specifying environment interaction
  good for controlling a character—fewer parameters

## Slide 10: Notations
: vector represented in coordinate frame i
: global position of the origin of coordinate frame i (global position of the ith joint)
: rotation matrix that transforms a vector from coordinate frame i to coordinate frame j, i.e.,

## Slide 11: Forward Kinematics

## Slide 12: Forward Kinematics by Composing Transformations
End Effector
Relative rotation from the local coordinate of parent link to
the local coordinate of the child link
Notes: Moving local coordinate along the joint-link chain.

## Slide 13: With simplified notations
?
Base
End Effector

## Slide 14: Acclaim Format
Skeletal animation file format including
  .ASF: Skeleton file
  .AMC: Motion file
All information in ASF file is specified with respect to the global coordinate, while all information in AMC file is specified with respect to the local coordinate.

## Slide 15: ASF File
Describes the local frame of each bone of a neutral (zero) pose in the global coordinate, e.g. Euler angle in xyz order,
We need to compute the relative transformation and the unit-length bone direction vector in local coordinate
begin
id 2
name lfemur
direction 0.342 -0.939 0
length 7.113
axis 0 0 20 XYZ
dof rx ry rz
limits (-160.0 20.0)
(-70.0 70.0)
(-60.0 70.0)
end

## Slide 18: AMC File
#!OML:ASF F:\VICON\USERDATA\INSTALL\rory3\rory3.ASF
:FULLY-SPECIFIED
:DEGREES
1
root 3.1294 17.6906 0.576147 -69.7364 88.7134 -68.7451
lowerback 5.37529 -0.419929 3.55267
upperback -1.47894 -0.3644 -1.32457
thorax -4.58452 -0.299522 -3.33877
lowerneck -3.64552 -5.65816 -4.72229
upperneck 4.19034 -7.74441 9.40555
head 2.64463 -3.6745 3.67041
rclavicle 1.2921e-015 1.55052e-014
rhumerus -39.2113 -25.8219 -71.2854
rradius 20.028
rwrist 28.2698
rhand -0.838087 16.263
rfingers 7.12502
rthumb 24.7874 -12.1506
lclavicle 1.2921e-015 1.55052e-014
lhumerus -35.6109 24.573 71.3578
lradius 16.6086
lwrist 15.9001
lhand -12.5773 10.6855
lfingers 7.12502
lthumb 13.5007 40.2279
rfemur 1.2602 0.329943 20.7559
rtibia 13.9379
rfoot -15.3822 -1.1112
rtoes -8.02936
lfemur 3.52626 0.806532 -14.1882
ltibia 8.14895
lfoot -11.1811 0.939771
ltoes -6.61339

## Slide 19: Forward Kinematics in ASF/AMC
begin
id 2
name lfemur
direction 0.342 -0.939 0
length 7.113
axis 0 0 20 XYZ
dof rx ry rz
limits (-160.0 20.0)
(-70.0 70.0)
(-60.0 70.0)
end

## Slide 20: Inverse Kinematics
Base
End Effector=P

## Slide 21: Redundancy in IK
Our example
  2 equations (constraints)
  3 unknowns
  Multiple solutions exist!
This is not uncommon!
  see how you can move your elbow while keeping your finger touching your nose

## Slide 22: Other problems in IK
Infinite solutions

## Slide 23: Other problems in IK
No solutions

## Slide 24: Why Is IK hard?
Redundancy
Natural motion
  joint limits
  minimum jerk
  style?
Singularities
  ill-conditioned matrix
  shown later

## Slide 25: Solving Inverse Kinematics
Analytic method
Inverse-Jacobian method
Optimization-based method
Example-based method

## Slide 26: Analytic Method
(X,Y)
L1
L2
q1
q2
Goal

## Slide 27: Analytic Method (cont.)
(X,Y)
L1
L2
q1
qT
180- q2
X
Y

## Slide 28: Cosine Law
A
B
C
a

## Slide 29: Analytic Method
(X,Y)
L1
L2
q1
qT
180- q2
X
Y

## Slide 30: Inverse-Jacobian method
When linkage is complicated
Iteratively change the joint angles to approach the goal position and orientation

## Slide 31: Jacobian
Jacobian is the n by m matrix relating differential changes of q to differential changes of p (dp)
Jacobian maps velocities in joint space to velocities in cartesian space

## Slide 32: Kinematic Interpretation of Jacobian

## Slide 33: Example: Jacobian for a 2D arm
Let’s say we have a simple 2D robot arm with two 1-DOF rotational joints:
θ1
θ2
• p=[px py]

## Slide 34: Jacobian for a 2D arm
The Jacobian matrix J(θ) shows how each component of p varies with respect to each joint angle

## Slide 35: Jacobian for a 2D arm
Consider what would happen if we increased θ1 by a small amount. What would happen to p ?
θ1
•

## Slide 36: Jacobian for a 2D arm
What if we increased θ2 by a small amount?
θ2
•

## Slide 37: Jacobian for a 2D arm
•
θ1
θ2

## Slide 38: Computing Jacobian analytically
A simple example:
You can imagine how computing Jacobian gets ugly when there are multiple joints!

## Slide 39: Computing Jacobian geometrically
Instead of computing Jacobian analytically, we can take a geometric approach to compute it
Let’s say we are just concerned with the end effector position p for now.
  This also implies that the Jacobian will be an 3×N matrix where N is the number of DOFs
  For each DOF of a joint, we analyze how p would change if the DOF changes

## Slide 40: Rotational DOFs
Let’s consider a 1-DOF rotational joint first
We want to know how the global position p will change if we rotate around the axis.
θ1
•
unit-length rotation
axis vector

## Slide 41: Rotational DOFs
ai: unit length rotation axis in world space
ri: position of joint pivot in world space
p: end effector position in world space
•
•

## Slide 42: 3-DOF Rotational Joints
Once we have each axis in world space, each one will get a column in the Jacobian matrix
At this point, it is essentially handled as three 1-DOF joints, so we can use the same formula for computing the derivative as we did earlier:
We repeat this for each of the three axes

## Slide 43: Iterative IK Using Inverse Jacobian
Linearize about qk locally
Small increments
P
P+dP
Pgoal

## Slide 44: Jacobian may not be invertible!
Non-square matrix
  pseudo inverse
Singularity
  causes infinite joint velocities
  occurs when any cannot achieve that is not perpendicular to the arm

## Slide 45: Remedy to Singularity Problem
Add redundancy
  add more joints to the original joint chain
  (more DOFs are added)
  Jacobian matrix is not square
Use pseudo inverse of Jacobian!

## Slide 46: Pseudo Inverse of the Jacobian

## Slide 47: Adding more control to IK
Pseudo inverse computes one of many possible solutions that minimize joint angle velocities
IK using pseudo inverse Jacobian may not provide natural poses
A control term can be added to the pseudo inverse Jacobian solution
The control term should not add anything to the velocities, that is
control term

## Slide 48: Control Term Adds Zero Linear Velocities
A solution of this form
…it doesn’t affect the desired configuration
But it can be used to bias
The solution vector
When put into this formula
Like this
After some manipulation, you can show that …

## Slide 49: Null space
The control term C is in the null space of J
The null space of J is the set of vectors which have no influence on the constraints

## Slide 50: Utility of Null Space
The null space can be used to reach secondary goals
Or to find natural pose / control stiffness of joints

## Slide 51: Optimization-based Method
Formulate IK as an nonlinear optimization problem
  Example
  Objective function
  Constraint
  Iterative algorithm
Nonlinear programming method by Zhao & Badler, TOG 1994

## Slide 52: Objective Function
“distance” from the end effector to the goal position/orientation
Function of joint angles : G(q)
Base
End Effector
Goal
distance

## Slide 53: Objective Function
Position Goal
Orientation Goal
Position/Orientation Goal
weighted sum

## Slide 54: Nonlinear Optimization
Constrained nonlinear optimization problem
Solution
  standard numerical techniques
  MATLAB or other optimization packages
  usually a local minimum
  depends on initial condition
joint limits
limb coordination

## Slide 55: Example-based Method
Utilize motion database to assist IK solving
IK using interpolation
  Rose et al., “Artist-directed IK using radial basis function interpolation,” Eurographics’01

## Slide 56: Example-based Method (cont.)
IK using constructed statistical model
  Grochow et al., “Style-based inverse kinematics,” SIGGRAPH’04
  Provide the most likely pose based on given constraints

## Slide 57: Example-based Method (cont.)
Constructed pose space (training, extrapolated)

## Slide 58: Videos
“Style-based inverse kinematics”

## Slide 59: References
Zhao and Badler, "Inverse kinematics positioning using nonlinear programming for highly articulated figures," ACM TOG 1994.
Rose et al., “Artist-directed IK using radial basis function interpolation,” Eurographics’01
Keith Grochow, Steven L. Martin, Aaron Hertzmann and Zoran Popovic , "Style-based inverse kinematics," SIGGRAPH'04.